Appendix B: Storm Damage Protocol for all Field Sites

Note this protocol is adapted from: Peck, D.V., J.M. Lazorchak, and D.J. Klemm (editors). 2003 ,Environmental Monitoring and Assessment Program  Surface Waters: Western Pilot Study  Field Operations Manual for Wadeable Streams, Unpublished draft. EPA/XXX/X-XX/XXXX. U.S. Environmental Protection Agency, Washington, D.C. http://www.epa.gov/emap/html/pubs/docs/groupdocs/surfwatr/field/ewwsm01.html

Please provide photographic documentation of any storm damage noticed at study site.

Sample Storm Damage Assessment forms are contained in Appendix B.

5.1  Wind throw Assessment

- Within visual range note evidence of recent wind thrown trees.

  - If no evidence, check no evidence box on Damage Assessment form.

  - If evidence estimate approximate percentage of trees wind thrown.

- Within study area or adjacent to study reach note evidence of wind thrown trees within 10m riparian margin either side of bankfull level. If Yes complete Wind Throw Damage Form

- If no evidence, check no evidence box on Damage Assessment form.

- If evidence approximate percentage of trees wind thrown.

- Note evidence of wind thrown trees partially of fully in bankfull stream bed within study area or study reach.

- If no evidence, check no evidence box on Damage Assessment form.

- If evidence note

    - Number of fallen trees with large end diameter in following classes (1 = 0.1 < 0.3 m; 2 = 0.3 < 0.6 m; 3 = 0.6 < 0.8 m; and 4 = > 0.8 m).

    - Length type in logs that are 1.5 – 5 m long, 5 – 15 m and > 15 m.

  - Recent Flood and Debris Torrent Damage Assessment

- Within or adjacent to study reach note evidence of recent torrent scouring that have scoured away stream banks or damaged riparian vegetation on banks and gravel bars.

- If no evidence, check no evidence box on Torrent Damage Assessment form.

- If  evidence complete Torrent Damage Assessment form

- Within or adjacent to study reach note evidence of massive deposits of sediment, logs and other debris in reach.

- If no evidence, check no evidence box on Torrent Damage Assessment form.

- If evidence complete Torrent Damage Assessment form